## Slide 1: ROS ACTION
21AIE213 - Robot Operating System and Robot Simulation

## Slide 2: Previous Section
ROS Service
Turtlesim ROS Service
Creating ROS Service
Example Service Creation
Implementing a Service
  Creating a Server
  Creating a Client

## Slide 3: Section Overview
ROS Action
Turtlesim Action Service
Defining an Action
Example ROS Action
Implementing ROS Action Service
  Creating a Action Server
  Creating a Action Client

## Slide 4: ROS Action
ROS services, which are useful for synchronous request/response interactions.
Services are handy for simple get/set interactions like querying status and managing configuration, they don’t work well when you need to initiate a long-running task.
For example, imagine commanding a robot to drive to some distant location; call it goto_position . The robot will require significant time to do so.
The exact amount of time impossible to know in advance, since obstacles may arise that result in a longer path.
Client will be blocked until a response comes

## Slide 5: ROS Action
ROS actions are the best way to implement interfaces to time-extended, goal-oriented behaviours like goto_position.
While services are synchronous, actions are asynchronous.
Similar to the request and response of a service, an action uses a goal to initiate a behaviour and sends a result when the behavior is complete.
But the action further uses feedback to provide updates on the behaviours' progress toward the goal and also allows for goals to be cancelled.
Actions are themselves implemented using topics. An action is essentially a higher-level protocol that specifies how a set of topics (goal, result, feedback, etc.) should be used in combination.

## Slide 6: ROS Action
Image Courtesy: Prof. Anis koubaa

## Slide 7: ROS Action

## Slide 8: ROS Action
Action Client
Goal
Action Server
Action Client
Action Client
Action Server
Action Server
Feedback
Result
ActionLib

## Slide 9: Turtlesim Action Service

## Slide 10: Listing actions

## Slide 11: Running teleop node

## Slide 12: Listing actions in teleop node

## Slide 13: Listing action

## Slide 14: Sending action request

## Slide 15: Cancelling action

## Slide 16: Aborting action

## Slide 17: Action data type

## Slide 18: Command Line Action Client

## Slide 19: COMMAND LINE ACTION CLIENT with feedback

## Slide 20: Defining an Action
Five Steps to Define New ROS Action
1. Create a new folder named "action" in root of the package
2. Inside action folder create a new action file named "ActionName.action"
3. Define the new action in the action file
4. Update CMakeList.txt and package.xml file to compile the new action into language-specific implementations
Build the package and Source the devel/setup.bash file

## Slide 21: ROS Action Format
ActionName.action​
GoalType1 GoalFieldName1​
GoalType2 GoalFieldName2​
---​
ResultType1 ResultFieldName1
ResultType2 ResultFieldName2
---
FeedbackType1 FeedbackFieldName1
FeedbackType2 FeedbackFieldName2
​

## Slide 22: Compiling the Service
Before compiling the new service, changes have to be made in CMakeList.txt and package.xml files to make catkin identify the new message
In package.xml file, add the below lines

## Slide 23: COMPILING THE Service
In CMakeList.txt file do the following changes
Go to the root of your catkin workspace, and build the package
Type command : source catkin_workspace/devel/setup.bash
Will create new message named Your_Service, Your_ServiceRequest and Your_ServiceResponce

## Slide 24: Example ROS Action
Fibonacci action
This action gives us the Fibonacci series given the order
Along the way, it should tell us periodically the intermediate series
When it’s done, it should tell us full series

## Slide 25: EXAMPLE Action CREATION
Create a package named "fibonacci_action_interface" and a sub directory named action
Store Fibonacci.action file in the action directory.
Change the configuration files accordingly
Build the package and source the devel/setup.bash
Create a new package named "fibonacci_server_client" and write a python server and client for the Fibonacci action
  Change the setup.py file to enter the starting point

## Slide 26: Fibonacci Action – Action Format

## Slide 27: Fibonacci Action - Server

## Slide 28: FIBONACCI ACTIOn SERVER– cHECKING

## Slide 29: FIBONACCI ACTION – SERVER Feedback

## Slide 30: FIBONACCI ACTION SERVER Feedback – CHECKING

## Slide 31: FIBONACCI ACTION – Client

## Slide 32: FIBONACCI ACTION CLIENT- Output

## Slide 33: Thank You !!!